HEXAGONAL BOLTS WITH REDUCED HEAD PRODUCT GRADE B Construction and dimensions GOST 7796-70 Extract CONTRACT № PB/835606213601

HEXAGONAL BOLTS WITH REDUCED HEAD

PRODUCT GRADE B

Construction and dimensions

GOST 7796-70

Extract

| HEXAGONAL BOLTS WITH REDUCED HEADS PRODUCT GRADE B Construction and dimensions | GOST 7796-70 Extract |
| --- | --- |

1. Present standard deals with hexagonal bolts with reduced head of product grade B with thread diameter ranging from 8 to 48 mm.

2. Design and dimensions of bolts should correspond to those specified in drawing and in table 1 and 2.

3. Thread as per GOST 24705-81. Run out and undercut of thread – as per 
GOST 27148-86. Ends of bolts – as per GOST 12414-86.

4. Radius under the head – as per GOST 24670-81.

5. Tolerances for dimensions, deviation of shapes and location of surfaces and methods of checking, not established by the present standard, are as per GOST 1759.1-82.

6. Permissible surface defects of bolts and methods of checking are as per 
GOST 1759.2-82.

7. Bolts of make 1 and 2 with head height equal to k1, may be manufactured as per agreement between manufacturer and user.

8. Alternate make of heads are set by manufacturer.

9. Bolts, with diameter of smooth part of shank d1 approximately equal to pitch diameter of threads, may be manufactured as per agreement between manufacturer and user.

10. Bolts of make 1 and 2 with rises on end face of surface of heads with dimensions, not reducing the strength of head may be manufactured for applying marking symbols, during this, the depth of rises should be not more than 0.4 k.

11. Technical requirements – as per GOST 1759.0-87.

mm 											Table 1

| Nominal diameter of thread d | 8 | 10 | 12 | (14) | 16 | (18) | 20 | (22) | 24 | (27) | 30 | 36 | 42 | 48 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Thread pitch | Coarse | 1.25 | 1.5 | 1.75 | 2 | 2 | 2.5 | 2.5 | 2.5 | 3 | 3 | 3.5 | 4 | 4.5 | 5 |
|  | Fine | 1 | 1.25 | 1.25 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 2 | 2 | 2 | 3 | 3 | 3 |
| Diameter of rod d1 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 27 | 30 | 36 | 42 | 48 |
| Dimension <<for wrench>> S | 12 | 14 | 17 | 19 | 22 | 24 | 27 | 30 | 32 | 36 | 41 | 50 | 60 | 70 |
| Height of heads k | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 15 | 17 | 20 | 23 | 26 |
| Height of head k1 | 5.3 | 6.4 | 7.5 | 8.8 | 10.0 | 12.0 | 12.5 | 14.0 | 15.0 | 17.0 | 18.7 | 22.5 | 26.0 | 30.0 |
| Diameter of specified circumference e, not less than | 13.1 | 15.3 | 18.7 | 20.9 | 23.9 | 26.2 | 29.6 | 33.0 | 35.0 | 39.6 | 45.2 | 55.4 | 66.4 | 76.9 |
| dw, not less than | 10.5 | 12.5 | 15.5 | 17.2 | 20.1 | 22.0 | 24.8 | 27.7 | 29.5 | 33.2 | 38.0 | 46.6 | 55.9 | 64.7 |
| hw | not less than | 0.15 | 0.20 | 0.25 |
|  | not more than | 0.6 | 0.8 |
| Diameter of hole in rod d3 | 2.0 | 2.5 | 3.2 | 4.0 | 5.0 | 6.3 | 8.0 |
| Diameter of hole in head d4 (deviation limit H15) | 2.5 | 3.2 | 4.0 | 5.0 |
| Distance between supporting surface and axis of hole in head l2 (deviation limit js15) | 2.8 | 3.5 | 4.0 | 4.5 | 5.0 | 6.0 | 6.5 | 7.0 | 7.5 | 8.5 | 9.5 | 11.5 | 13.0 | 15.0 |

Note: Dimensions of bolts, specified in brackets, are not recommended to use.

Note:

1. Bolts with dimensions of length, specified in brackets, are not recommended to use.

2. Bolts, for which value b is located above the thick line, may be manufactured with thread length upto head.

Example of conventional designation of bolt for make 1, having diameter of thread d = 12 mm, length l = 60 mm, having coarse pitch of thread with tolerance field 6g, strength class 5.8 without coating.

Bolt M12-6g x 60.58  GOST 7796-70

Same with, make 2, having fine pitch of thread with tolerance field 6g, strength class 10.9, made from steel grade 40X, with coating thickness 6 microns:

Bolt 2M12x1.25-6g x 60.10.9.40X.016  GOST 7796-70